## Slide 1: ELEC 3204 Major Project
Arnav Dhir | Devagya Budhiraja | Shun Ying Wong
Washing Machine

## Slide 2
Washing Machine
Our Set up

## Slide 3: Washing Machine
Open Loop
Closed Loop
Mimics real washing modes:
Wash, clean, and spin
Motor spins in both directions at various speeds
Time-based control with no feedback needed
Motor runs in one direction at target speed
Add weight → RPM drops → system compensates
Feedback control adjusts input to maintain RPM
🧑‍💻 GUI for User input
🛑 Emergency stop for safety

## Slide 4
Washing Machine
Open Loop
Closed Loop
Mimics real washing modes:
Wash, clean, and spin dry
Motor spins in both directions at various speeds
Time-based control with no feedback needed
Motor runs in one direction at target speed
Add weight → RPM drops → system compensates
Feedback control adjusts input to maintain RPM
GUI for User input
🛑 Emergency stop for safety

## Slide 5: Open Loop
Normal Soil: Wash – Clean – Spin dry
Washing Machine
Closed Loop
Mimics real washing modes:
Wash, rinse, and spin
Motor spins in both directions at various speeds
Time-based control with no feedback needed
Motor runs in one direction at target speed
Add weight → RPM drops → system compensates
Feedback control adjusts input to maintain RPM
🧑‍💻 GUI for User input
🛑 Emergency stop for safety
3-step motor operation with timed fixed-speed control
Wash: 20 RPM for 21.5s
Clean: 40 RPM for 8.5s
Spin dry: 80 RPM for 5s
  Total duration: 35s
Wash
Clean
Spin

## Slide 6: Washing Machine
Open Loop
Closed Loop
Mimics real washing modes:
Wash, clean, and spin
Motor spins in both directions at various speeds
Time-based control with no feedback needed
Motor runs in one direction at target speed
Add weight → RPM drops → system compensates
Feedback control adjusts input to maintain RPM
🧑‍💻 GUI for User input
🛑 Emergency stop for safety

## Slide 7
Closed Loop
Arduino controls motor via PWM signal to the H-bridge
Motor speed is measured using encoder feedback through EN_A & EN_B
Real-time speed is compared with target RPM inside Arduino
If motor slows down due to added weight, ➜ Arduino increases PWM duty cycle to restore RPM
This loop continues where its constantly correcting error → That’s negative feedback

## Slide 8: Washing Machine
Open Loop
Closed Loop
Mimics real washing modes:
Wash, rinse, and spin
Motor spins in both directions at various speeds
Time-based control with no feedback needed
Motor runs in one direction at target speed
Add weight → RPM drops → system compensates
Feedback control adjusts input to maintain RPM
GUI for User input
🛑 Emergency stop for safety
ADD IMAGE
OF GUI
Load-Sensitive Control
RPM adjusts based on weight
 Light load = higher RPM  Heavy load = reduced RPM
Weight added

## Slide 9: Thank You
“BabyGirl”
“Justified GirliePop”
“Oompaa Loompaa”